## Slide 1: Introduction to Verilog

## Slide 2: Overview of Verilog
Resemblance to C: case sensitive, same style comments, operators, etc.
Two standards: Verilog-1995, Verilog-2001, both supported by ISE
Easy to write, and easy to make mistakes

## Slide 3: Behavioral vs Synthesizable code
Historically Verilog has always served two functions:
Describe your digital logic design in a high-level way instead of using schematics (synthesizable code).
Model elements that interact with your design (behavioral models/testbenches)
You should always have a clear conscience of whether you are writing behavioral or synthesizable code.
Better yet, know what your synthesizable code translates to in physical hardware.

## Slide 4: Data Values
Values: 1, 0, x/X (unknown), z/Z (high impedance)
Radices: d(decimal), h(hex), o(octal), b(binary)
Format: <size>’<radix><value>
  123 // default: decimal radix, unspecified width
  ‘d123 // ‘d = decimal radix
  8‘h7B // ‘h = hex radix
  ‘o173 // ‘o = octal radix
  ‘b111_1011 // ‘b = binary radix, “_” are for readability
Signed number (rarely used):
  8’shFF (8-bit twos-complement representation of -1)

## Slide 5: Operators
Bitwise: ~a, a&b, a|b, a^b, a~^b
Reduction: bitwise operation on a single operand and produces one bit result.
&a, ~&a, |a, ~|a, ^a, ~^a
Example: ^4’b1001 = 1’b0
Logical: output one bit result
!a, a&&b, a||b, ==/!=, ===/!== (also compares x/z)
Arithmetic: +,-,*,/,% (mod, takes the sign of operand 1)

## Slide 6: Operators, ctd.
Can you tell the difference between the following expressions? What are the sizes of each expression and what do they mean?
Declaration: wire [31:0] a,b
a & b
a && b
(&a) & (&b)
(&a) && (&b)
&(a && b)
a && (&b)

## Slide 7: Operators, ctd.
Shift: <<, >>(logical)
<<<, >>> (arithmetic)
Conditional: sel ? a : b
Concatenation: {a, b}
Replication: {n{m}}
Assignment: =(blocking), <= (non-blocking)
Good reference: http://www.asic-world.com/verilog/operators2.html

## Slide 8: Basic building block: modules
port: input / output / inout
Signal declarations: wire [3:0] a;
  Rule-of-thumb: stick to [MSB:LSB]
Concurrent logic blocks, one of the following:
  continuous assignments
  initial blocks (only used in behavioral modeling)
  always blocks (either sequential or combinational)
  forever blocks (only used in behavioral modeling)
Instantiations of sub-modules
module top(a, b, ci, s, co
);
input a, b, ci;
output s, co;
wire s;
reg g, p, co;
assign s = a ^ b ^ ci;
// combinatorial always
// block using begin/end
// always @* is Verilog-2001
always @* begin
g = a & b;
p = a | b;
co = g | (p & ci);
end
endmodule

## Slide 9: Always Block: Sensitivity list
Level sensitive: changes to any signals on the sensitivity list will invoke the always block. Used in combinational circuits.
always @ (a or b) / always @* (verilog-2001, recommended)
Edge sensitive: invoke always block on specified signal edges. Used in sequential circuits.
always @ (posedge clk or posedge reset)

## Slide 10: Always Block: case, if/else
case (sel)
val0: statements
val1: statements
…
default: statements
endcase
if (condition)
statements
else if (condition)
statements
…
else
statements

## Slide 11: Always Blocks: case, if/else ctd.
module ALU(a, b, f, z
);
input [3:0] a, b;
input [1:0] f;
output reg [3:0] z;
always @(*)
z = 4’bx; (#1)
case (f)
0: z = a + b;
1: z = a * b;
2: z = a & b;
3: z = a | b;
default: z = 4‘bx; (#2)
endcase
endmodule
if/else or case statement fails to cover all cases  inferred latch
Example:
if (x == 2’b00)
z = a;
else if (x == 2’b01)
z = b;
What about other cases? The circuit will hold previous value
To avoid: add #1 or #2

## Slide 12: Always Block: Looping (while, for, repeat)
while (condition)
statements
for (initialization; condition; increment)
statements
repeat (n)
statements

## Slide 13: Data types: wire, reg
Variables must be declared before used; wire/reg are the most common data types.
wire:
models basic wire that holds transient values
only wires can be used on the LHS of continuous assign statement
input/output port signals default to wire
reg:
anything that stores a value
can appear in both combinational and sequential circuits
only regs can be used on the LHS of non-continuous assign statement
Reference: http://www.asic-world.com/tidbits/wire_reg.html

## Slide 14: Wire vs. reg
When to use wire:
Left hand side of “assign”
wire s;
assign s = a ^ b ^ ci;
When to use reg:
Left hand side of “=” or “<=” in “always” blocks
reg g, p, co;
always @* begin
g = a & b;
p = a | b;
co = g | (p & ci);
end

## Slide 15: Sequential circuit example: modulo 64 counter
module counter(clk, rst, out
);
input clk, rst;
output [5:0] out;
reg [5:0] out;
always @(posedge clk or posedge rst)
begin
if (rst)
out <= 6'b000000;
else
out <= out + 1;
end
endmodule

## Slide 16: Blocking/Non-blocking assignments
reg B, C, D;
  always @(posedge clk)
    begin
    B = A;
    C = B;
    D = C;
  end
reg B, C, D;
  always @(posedge clk)
    begin
    B <= A;
    C <= B;
    D <= C;
  end

## Slide 17: Assignment operator guidelines
Sequential logic: use nonblocking (<=)
Pure combinational logic in “always” block: use blocking (=)
Do not mix blocking/non-blocking in the same “always” block
Both sequential and “combinational” logic in the same “always” block: use non-blocking (<=)
y <= a ^ b;
Recommendation: in complex sequential circuit, use two always blocks, one for combinational circuit, one for state update.

## Slide 18: Module instantiation
Achieve hierarchical design by using other modules inside one module.
Recommended format:
type name (.port1(w1),.port2(w2)......);
Port order doesn’t matter
Unused output port allowed
Name must be unique within module

## Slide 19: Example
module half_adder(a, b, x, y
);
input a, b;
output x, y;
assign x = a & b;
assign y = a ^ b;
endmodule
module full_adder(a, b, ci, s, co
);
input a, b, ci;
output s, co;
wire g, p, pc;
half_adder h1(.a(a), .b(b), .x(g), .y(p));
half_adder h2(.a(p), .b(ci), .x(pc), .y(s));
assign co = pc | g;
endmodule

## Slide 20: Schematics output

## Slide 21: Testbench
Testing is important and engineers spend more time testing for complex digital circuits.
Procedures for creating testbench:
Instantiate unit under test (uut)
Provide input for uut: clk, rst, data...
Simulate and verify behavior

## Slide 22: Initial block
initial begin
// Initialize Inputs
clk = 0;
rst = 0;
// Wait 100 ns for global reset to finish
#100;
// Add stimulus here
rst = 1;
#20 rst = 0;
// add verification routine here
#1000 $finish;
end
Initial block starts execution at time 0.
#n : wait n time units
$finish: stop simulation

## Slide 23: Parameter
module ALU #(parameter W=4)(a, b, f, z);
input [W-1:0] a, b;
input [1:0] f;
output reg [W-1:0] z;
always @(*)
case (f)
0: z = a + b;
1: z = a * b;
2: z = a & b;
3: z = a | b;
default: z = {(W){1'bx}};
endcase
endmodule

## Slide 24: Instantiation of parameterized module:
Default parameter W=4. Instantiate a 16-bit ALU:
Format:
type #(params) name (ports);
Example:
ALU #(.W(16)) alu16 (.a(a), .b(b), .f(f), .z(z));

## Slide 25: References
MIT 6.111 course notes,
http://web.mit.edu/6.111/www/f2013/index.html
Verilog in one day,
http://www.asic-world.com/verilog/verilog_one_day.html
Wire vs. Reg,
http://inst.eecs.berkeley.edu/~cs150/Documents/Nets.pdf
Sunburst Design (Read on assignment operators)
http://www.sunburst-design.com/papers/
5. ISE Quick Start Guide
  http://cseweb.ucsd.edu/classes/wi11/cse141L/Media/Quick-Tutorial-11.pdf
  6. Washington CSE 467 Notes
  https://courses.cs.washington.edu/courses/cse467/03wi/Verilog3.pdf